## Slide 1: Surface Finishing
Submitted to : Md. Shariful Islam
Md. Maksimul Islam
Welcome to Our
Presentation

## Slide 2: Objectives
    To understand surface finishing
    To know different types of surface
    finishing
    To learn the process of surface finishing.

## Slide 3: What is Surface Finishing ???
art of covering surface
Final touch of any construction
Column
Slab
Beam

## Slide 4: Purposes of Surface Finishing
Without
With
to protect the surface from weathering effect
to make the surface decorative
to provide a smooth surface
Without
With

## Slide 5: Types of Surface Finishing
Plastering
Painting
Pointing
Tiles Fitting
Wall paper
Wall Finishing
      Interior Wall Finishing
      Exterior Wall Finishing
Floor Finishing
Mosaic

## Slide 6: Plastering
Internal and external application of solid materials
Solid materials comprise of
            Sand
            Lime or cement
            Other additives
Materials are applied wet in coats.
To provide smooth, hard surface finish

## Slide 7: Purposes of Plastering
  To provide an even, smooth, regular, clean and durable finished surface.
  To protect the surface
  To conceal the defective workmanship.

## Slide 8: Materials and tools
Cement
Bulk Coarse Sand
Plumb Bob
Trowel
Leveler
Notes: Check the Fm

## Slide 9: Steps of Plastering
Preparation of Mortar
Applying Mortar to Wall
    Curing
Fully Plastered Wall
Leveling the applied Mortar
    Checking if the wall is vertical

## Slide 10: Steps of Plastering
Preparation Of Mortar
Applying Mortar to Wall
Cement : Sand :-
for wall 1:4
for ceiling 1:3
Mixing of cement and bulk sand.
The look of the wall after applying mortar

## Slide 11: Steps of Plastering
Leveling the applied Mortar
Checking if the wall is vertical
Leveling with
  Trowel
  Leveling Rod
Plumb Bob

## Slide 12: Steps of Plastering
Plastered Wall
Things to be taken care of
water should not be used
while applying mortar
Curing should start after
24 hours.

## Slide 13: Pointing
Process:
    Removal of dust from joints
    Washing the surface
    The mortar is then carefully placed
    The finished surface is
    well-watered for a period of time
Final treatment done to the joints of the masonry
Purpose:
      To increase durability of exterior wall
      To improve the appearance

## Slide 14: Painting
Application of oil paint to timber, metal and plaster.
Paint is
    A protective or decorative layer.
    Composed of i. liquid medium
        ii. A coloring agent
        iii. Other agent
    Applied in Coats
to provide a pleasant appearance.
Notes: Liquid medium- linseed oil or water
Coloring agent – pigment
Other agents - to flow or drying of paint

## Slide 15: Materials and tools
PAINT
Weather coat
Sealer
Roller
Putty
Notes: Nippon Vinilex 5101 Water-Based Wall Sealer is suitable for masonry surfaces. It is formulated to prevent deterioration of emulsion paints by alkalinity of surfaces. This wall sealer is recommended for use in both interior and exterior plastered walls, ceilings, plaster, brickwork and wall boards. Based on specially formulated acrylic it is designed to provide maximum protection against alkali and moisture, enhancing the performance of top coat. A water-based wall sealer stops liquid water from entering the surface, but allows water vapour out. It is a breathable product that can be applied to brick, concrete block, stucco or any masonry material.
Weather coat-Specially formulated weather beating formulation that gives a flexible, crack resisting, high gloss finish.
Putty-it easier to paint the wall. They told me that to use putty makes the wall flat and look nicer and you are able to paint the wall easily

## Slide 16: Steps of Painting
Stone Throwing
Applying Sealer
Applying Weather Coat
Painted wall
Applying Paint
Painted wall
Applying Putty
Interior Wall
Exterior Wall
Notes: All the application are coating

## Slide 17: Steps of painting
Stone throwing
Applying Sealer
Stone
Removing the roughness of the wall.
Sealer : Water:-
2:1
Applying the first coat

## Slide 18: Steps of painting Interior wall
Making of Putty
Applying Putty
Applying putty along a line
Furnace asbestos
A glue type material
Composed of
        Chalk Powder
        Enamel Paint
        Plastic Paint
        Water

## Slide 19: Steps of painting
Applying Paint
In Interior wall, paint is used after some preparation
In Exterior wall weather coat is used
In both cases paint is applied in 3 coats
Second coat is applied minimum 7 days after the first coating

## Slide 20: Wallpaper
Pasting Wallpaper
Decorated Wall
A type of recent times interior
wall finishing
Wallpaper is
      Roll paper material
      Have printed pattern.
Pasted to wall or ceiling
Develops decorative finishing to
interior walls.

## Slide 21: Tiles Fitting
Fitting of tiles in the floor.
Tiles is
      A flat thin slab
      Made of fired clay,
      rubber, linoleum, etc.
      Square or rectangular
      and sometimes ornamental
To make the floor flat and decorative

## Slide 22: Materials and tools
Tiles
Cement
Bulk Sand
Grout
Tiles spacer
Hammer
Sponge and Bucket
Tiles Cutter

## Slide 23: How to Fit a tile ???
Checking if the floor is level
Tiling the total surface area
Chipping the floor or the wall
Laying a thin set of mortar
Fitting the tiles
Ceramic Floor Tiles
Filling in the joints with grout
spreading grout over the thin set

## Slide 24: fitting tiles
Checking if the floor is level
Tiling the total surface area
To find out the required amount of tiles needed for the work done.
Find out the center of the room with tape measure
For proper initialization of tiles fitting.
Done with a leveling tool such as spirit level
To ensure the progress of further work without problem

## Slide 25: fitting tiles
Chipping the floor or the wall
Chipping the floor with hammer
Appearance of a wall after chipping
Laying a thin set of mortar
Thin set of mortar
Grout

## Slide 26: fitting tiles
Spreading grout over the thin set of mortar
Fitting the tiles
Taking necessary measurement
fitting the tiles with hammer

## Slide 27: fitting tiles
Cutting the tile
Sometimes necessary to cover the extra space
Filling in the joints with grout
Filled with grout (made of white cement)
Joints between the tiles

## Slide 28: fitting tiles
Ceramic Floor Tile
Things to be taken care of
Good workmanship is a must
water screening test :
to check that no water
is penetrating through tiles

## Slide 29: Mosaic
Process:
      Cleaning the floor
      Preparing and applying the thin set
      Setting the mosaic in place over the thin set
      Continually to clean the mosaic surface
      Allowing the recommended thin set manufacturer time to dry.
      To grout the surface of the marble mosaic
made up from small pieces of glass and stone
provides durable walking surface

## Slide 30
Prepared By:
1004002 - Azmayeen Rafat Shahriar
1004007 - Sarsiz Alam
1004016 - S.Mm Mahmudul Haque
1004021 - Iftekhar Mahmud
1004026 - Md. Abdul Hannan Prodhan
1004032 - Shah Waliul Hoque Chowdhury
1004038 - Pritom Paul
1004046 - Sk. Md. Mashrur
1004051 - Mousumy Aktar
1004056 - Asaduzzaman Pintu
1004063 - Md Arafat Saklain