## Slide 1: Process of plasterwork
Presented by:
Group – 2
Student ID: 1104148-1104164

## Slide 2: Plasterwork:
The art of covering the surface of masonry work with a suitable material is called plastering.

## Slide 3: Why it is necessary
To protect the external surfaces against penetration of rain water and other atmospheric agencies
To give smooth surfaces in which dust and dirt can not lodge
To give decorative effect
To protect surfaces against vermin
To conceal inferior materials and defective workmanship

## Slide 4: Types:
A fine paste of mortar made by mixing cement with sand or fat lime with sand or surkhi in addition to sufficient quantity of water.
When cement is used as a binding material, the plaster is called cement plaster and if lime is used as the binding material, it is called lime plaster.
Other than these, Mud plaster, Stucco plasters are also included amongst various types.

## Slide 5: Suitability of different Types of plastering

## Slide 6: Cement Plastering:
External finishings
Internal renderings of common as well as important buildings
Damp conditions

## Slide 7: Lime Plastering
Internal renderings of buildings.
Not commonly adopted these days.

## Slide 8: Mud plastering
Adobe walls
Requires additional waterproofing.

## Slide 9: Stucco plastering
External as well as internal surfaces of buildings to provide an excellent finish
All types of decorative plasterworks

## Slide 10
DARBY
TROWELS
FLOATS
TOOLS OF PLASTERING

## Slide 11: Steps of plastering
Preparing Surface for Plastering
Wetting The Surface
Grouting
Covering with Mortar Paste
Leveling with Plumb Bob
Applying Second Layer
Leveling and Smoothing
Brushing with flower broom & Sponge

## Slide 12: Preparing Surface for Plastering
Raking the surface
Removing Efflorescence
Improving Adhesion

## Slide 13: Wetting The Surface
Ensuring Saturated condition of Bricks or surface to be plastered
Surface kept wet for at least 6 hours prior to plastering

## Slide 14: Grouting
Renders the function of glue in plastering

## Slide 15: Covering with Mortar Paste

## Slide 16: Leveling with Plumb Bob
Maintaining surface alignment

## Slide 17: Applying Second Layer

## Slide 18: Leveling and Smoothing

## Slide 19: Brushing with flower broom
Smoothing by sponge
Smoothing by broom

## Slide 20: Defects in plaster work
Blistering of plastered surface: Formation of small patches of plaster swelling out beyond the plastered surface, rising out of late slaking of lime particles in the plaster

## Slide 21
Cracking: caused by
Imperfect preparation
Structural defects
Discontinuity of surface
Movements in background or surface due to thermal expansion or rapid drying or shrinkage
Faulty workmanship

## Slide 22
Efflorescence:
Whitish crystalline substance on the surface due to presence of salts in plastering materials as well as building materials like brick, sand, cement even water.
Gives a very bad appearance and affects the adhesion of paint.
Can be removed by dry brushing and washing the surface repeatedly.

## Slide 23
Flaking: Formation of very loose mass of plastered surface due to poor bond between successive coats.
Peeling: Complete dislocation of some portion of plastered surface, resulting in the formation of a patch. This also results from imperfect bond.

## Slide 24
Popping: Formation of conical hole in the plastered surface due to presence of some particles which expand on setting.
Rust stains: Formed when plaster is applied on metal laths
Uneven surface : Happens because of poor workmanship

## Slide 25: Recommendations:
Brick and concrete surface joints
Plastering of outer surfaces
Curing
Modern implementations
Environmental friendly plasters

## Slide 26
T h a n k y o u