## Slide 1: Bangladesh University Of Engineering & Technology
Presentation On
WATER PROOFING OF BASEMENT
Presented By: Group 1
Sanjida Islam Archi
Shuvro Kumar Chakravorty
Khondokar Al Momin
Gazi Md Imran
Md. Lutfor Rahman
Ehshan ur Rahman
Md Shahadat Hossain
Md Saiful Islam
Md.Sajedur Rahman

## Slide 2: WHAT IS WATERPROOFING
Waterproofing is the formation of an impervious barrier
prevent water entering
escaping water from various sections of building structures
resistance to humidity or dampness

## Slide 3: Where Water proofing is needed
Internal areas :
bathrooms
shower recesses
laundries
toilets
External areas
roofs , planter boxes
podiums , balconies , terraces
retaining walls , Basement
swimming pools

## Slide 4: Water Proofing on Basement

## Slide 5: HOW WATER PERMEATES IN THE UNDERGROUND STRUCTURES
Soil contains a huge amount of water in its pores
water has its own pressure, varies with the depth, the hydrostatic pressure increases.
Soil itself has also its own pressure. This total pressure forces water to create cracks in Basement.

## Slide 6: HOW WATER PERMEATES IN THE UNDERGROUND STRUCTURES

## Slide 7: Where it is more necessary
In the areas where it rains often .
In the hilly area where underground water has a flow

## Slide 8: Water Damages In Basements
Shorter life span
Cracks
Corrosion
Weakening the joints
Swelling of plasters
Electrical Hazard
Deterioration of Building Facade

## Slide 9: Water Proofing Materials
Additives
Waterproof Cement
Ferrocement
Waterproof Membrane
Tar & Bitumen
Bentonite

## Slide 10: Additives
Krystol Mortar Admixture
Xypex Admix

## Slide 11: Waterproof Cement
Cement processed by
mixing water proofing
additives and epoxies

## Slide 12: Ferrocement
wire mesh mortar
6mm ~ 20 mm
Component Materials:
Cement
Aggregate (sand)
Water
Reinforcement

## Slide 13: Ferrocement
Ferrocement provides
higher tensile and flexural strength
resists corrosion
provide a crack free, tough dependable surface free
highly crack resistant
have excellent bond with the surface
highly impervious nature

## Slide 14: Water Proofing Membrane
Bitumenus Felts
Mastic Asphalts
Silicon
Epoxy
Different Polymers

## Slide 15
Felt Paper
Felt paper or asphalt felt paper is a sheet material
impregnated with bitumen (asphalt) , similar to tar paper
common grades
type 1 (number 15)
type 2 (number 30)

## Slide 16: Felt Paper
Felt Paper

## Slide 17: Felt Paper
Steps:
Rubbing Bitumen on the wall
Push china felt paper on the Bitumen layer
Use sand for tightening

## Slide 18: Tar & Bitumen
Bitumen (asphalt) is a mixed substance made up of organic liquids

## Slide 19: Tar & Bitumen
highly sticky
Viscous
waterproof
Characteristics Of Tar & Bitumen

## Slide 20: Bentonite
Bentonite is an absorbent aluminium phyllosilicate, impure clay consisting mostly of montmorillonite
Types Of Bentonite
Sodium Bentonite
Calcium bentonite
Potassium bentonite

## Slide 21: Stepss Of Water Proofing
taking proper consideration at the design stage
choosing the right product for the job
taking adequate preparation
managing the correct application

## Slide 22: Water Proofing For Simple Basement & Ordinary Soil

## Slide 23
Ferrocement layer on shore piles
Sand Fill
Brick wall
Retaining wall
Water Proofing for Deep Basement or Damp Soil

## Slide 24
Sand Fill
Brick wall
Retaining wall
Felt paper is placed on the external surface of the brick wall
Water Proofing for Deep Basement or Damp Soil

## Slide 25: Water Proofing for Deep Basement or Damp Soil
Sand
Water Proofing Membrane
( Polythene / Tar )
CC Layer
Reinforced Concrete
With Additives

## Slide 26: Cure
No permanent cure
Ferrocement and sodium
bentonite can be used in the
internal surface
Curing external surface is
difficult for deep basement
and deep excavation

## Slide 27: IMPORTANCE OF WATER PROOFING IN BANGLADESH
The soil of Bangladesh is mostly deposited by the numerous rivers
For the geographical environment of our country it rains a lot in the monsoon
the structures of our country are in a great risk to be attacked by ground water.

## Slide 29
Thank You

## Slide 30
Any Question