## Slide 1: Requirements for an Ideal Rail Section:
  The rail should have most economical section, consistent with strength, stiffness and durability
  The rail should have balanced distribution of metal in its various components
  The centre of gravity (c.g.) of rail section should preferably be very near to the centre of height of rail so that maximum tensile and compressive stresses are equal

## Slide 2: Requirements/Design Considerations for the components of an Ideal Rail Section:
The head of Rail should have adequate depth to
  Allow for vertical wear
  Reduce the contact stress between the rail and the wheel
  Reduce Metal Flow
  Provide desired lateral stiffness
Head:

## Slide 3: Requirements/Design Considerations for the components of an Ideal Rail Section:
The web of Rail should be sufficiently thick so as to
  Withstand the stresses due to the loads coming on rail
Web:

## Slide 4: Requirements/Design Considerations for the components of an Ideal Rail Section:
The foot of Rail should be sufficiently thick and wide enough to
  Withstand vertical and horizontal forces
  Prevent overturning
  Spread the load on large area of sleeper
Foot:

## Slide 5: Weight of Rail and its Relation to Axle Load:
Factors influencing the weight of rail and its cross-sections are:
  Heaviest axle load
  Gauge of track
  Maximum permissible speed
  Type and spacing of sleepers
  Depth of ballast cushion
  Nature of traffic
A rail is defined by its weight
45 kg rail means the weight of rail/meter length is 45 kg
90 lb rail means the weight of rail/yard length is 90 lb
Maximum Axle load (ton) = 560 X wt. of rail

## Slide 6: Length of Rail:
Present tendency is to adopt a rail of more length. The primary advantages of longer rail are:
  Eliminates joints
  Require less number of rail fastenings
  Low construction & Maintenance costs
  Smooth running of trains and comfort to passengers
Bangladesh, India, Srilanka have adopted standard rail lengths of-
        12.80 m for B.G
        11.89 m for M.G

## Slide 7: Length of Rail:
The length of rail is, however, restricted due to the following factors:
  Difficulties in manufacturing longer rails
  Transport, lifting & handling
  Bigger expansion joint
  Heavy internal thermal stress at fittings
Now a days, Welded rails are used specially for high speed tracks. Requirements of welded rails are-
  High performance elastic fasteners
  Heavy concrete sleepers

## Slide 8: Mode of Distresses of Rail:
The rail head gets worn out in course of time due to:
  Friction between rail and moving wheel
  Impact due to acceleration, deceleration and braking of wheels
  Abrasion by rail-wheel
  The effects of weathering like temperature, moisture change etc.
Eventually the results of wear of rails are-
  Loss of weight of rail
  Reduced fatigue strength of rail
1. Wear of rails:

## Slide 9: Mode of Distresses of Rail:
Depending upon the location-
  a)Wear on top of rail head (vertical wear)
  b)Wear on ends of rail (ends wear)
  c)Wear on sides of rail head (lateral wear)
a)Causes of vertical wear-
  Abrasion of wheel
  Stress concentration by wheel loads
  Impact of heavy loads
  Wheel burns (slipping of wheels)
  Grinding actions of sand particles between rail & wheel
  Corrosion of rail metal (near sea)
1. Wear of rails (cont.):

## Slide 10: Mode of Distresses of Rail:
Due to ends wear-
  Joint fittings become loose
  Settlement of ballast occur
  Sleepers at joints are depressed
  Contact surface between rail & sleepers are worn out
1. Wear of rails (cont.):
At expansion gaps, wheels of train have to take a jump.
The jumps impart a blow at the ends of rails.
Due to successive blows, the ends of rails get battered.
b)Wear at ends of rail

## Slide 11: Mode of Distresses of Rail:
Causes are-
  Centrifugal force causes grinding action of wheel flanges on the inner side of the outer rail
  Train cannot bend at curves; hence causes biting of the inner side of the outer rail by wheel flanges
  Wear on inner side of inner rail by slipping action of wheels on curves
1. Wear of rails (cont.):
The most destructive type of wear.
Occurs when tracks are laid on curves
c)Wear at sides of the head of rail

## Slide 12: Mode of Distresses of Rail:
Methods of reducing wear of rails are-
  Using special alloy steel
  Use of heavier rail
  Reduction of expansion gap
  Exchange of inner and outer rails on curves
  Introducing parallel check rails (usually worn out rails are used as check rails)
  Lubrication of gauge faces of outer rails in curves
  Providing super-elevation
  Conning of wheel & Tilting of rail
1. Wear of rails (cont.):