## Slide 1: CE 2111 Mechanics of Materials-I (Shear Force and Bending Moment)

## Slide 2: Shear Force and Bending Moment
The algebraic sum of the vertical forces at any section of a beam to the right or left of the section is known as shear force
A shear force diagram (SFD) is one which shows the variation of shear force along the length of the beam.
The algebraic sum of the moments of all the forces acting to the right or left of any section of a beam is known as bending moment
A bending moment diagram (BMD) is one which shows the variation of bending moment along the length of the beam.

## Slide 3: Guidelines for drawing SFD and BMD
Consider left or right portion of the section
Add the forces normal to the beam on one of the portion. If right portion of the section is chosen, a force on the right portion acting downward is positive while a force acting upward is downward
The positive values of shear force and bending moments are plotted above the base line and negative values below the base line
The shear force diagram increase or decrease suddenly i.e. by vertical straight line at a section where there is a vertical point load
The shear force between any two vertical loads will be constant and hence the shear force diagram between two vertical loads will be horizontal
Bending moment at any hinge or roller support, at the end of beam, is zero

## Slide 4: SIGN CONVENTIONS

## Slide 5
RA = wL
MA = wL2/2
RA
MA
A
B
Shear force at any section x from right end Vx = wx
Bending moment at any section x from right end Mx = wx*x/2 = wx2/2

## Slide 7
300N
500N
800N
R
M
R = 1600 N
M = 2350 N-m

## Slide 8
Shear force at D VD = 800N
Shear force at C VC = 800N + 500N = 1300N
Shear force at B VB = 800N+500N+300N = 1600N
Shear force at A VA = +1600N
Bending moment at the free end D is zero
Bending moment between D and C at a distance x from D Mx = -800*x
At C, x = 0.8m MC = -800*0.8 = 640N-m
Bending moment between B and C at a distance x from D Mx = -800*x – 500(x-0.8)
Bending moment between B and A at a distance x from D Mx = -800*x – 500(x-0.8) – 300(x-1.5)

## Slide 10: Draw SFD and BMD for the Cantilever Beam
RA = 1.5 kN
MA = 1.875 kN-m
RA
MA
A
B
C

## Slide 11
Consider any section between C and B Vx = 1.0*x kN
At B; x =0 VB = 0
At C; x = 1.5 VC = 1.5 kN
Between A and C there is no load, the shear will remain constant
Bending moment at any section between C and B, Mx = -1.0*x*x/2 = -x2/2
At B x =0 MB = 0
At C, x = 1.5 MC = -1.125 N-m
Bending moment between A and C, Mx = -(Load due to UDL)* (x-0.75) [ x =1.5-2.0m]
RA
MA
A
B
C

## Slide 13
RA = 7 kN
MA = 10 kN-m
RA
MA
A
B
3 kN

## Slide 14
Shear force at B VB = 3.0 kN
Shear force at any section x from free end
Vx = 3.0 + w*x = 3.0 + 2*x
At B x =0 VB = 3.0N
At A x = 2.0 VA = 3.0 + 2*2 = 7 N
Bending moment at any section from free end
Mx = -(3*x + 2*x*x/2) = - (3x + x2)
At B x =0 MB = 0
At A, x = 2 MA = -10 kN-m
Bending moment between A and C, Mx = -(Load due to UDL)* (x-0.75) [ x =1.5-2.0m]
RA
MA
A
B
3 kN

## Slide 16: Draw SFD and BMD for the simple Supported Beam
RA = RB = wL/2

## Slide 17
Consider any section at distance x from left support Vx = RL – w*x = wL/2 – w*x
At A, x=0 =>VA = wL/2
At B, x=L => VB = -wL/2
At C, x = L/2 => Vc = 0
Bending moment at any section x from A
Mx = RL*x – wx2/2 = w(Lx-x2)/2
At A, x=0 =>MA = 0
At B, x=L => MB = 0
At C, x = L/2 => Mc = wL2/8

## Slide 20
RB = 5 kN
RA = 4 kN

## Slide 21
Shear force at A = RA = 4kN
Shear force between A and C is constant and equal to 4 kN
Shear force at C VC = 4-3 = 1 kN
Shear force at D VD = 1-6 = -5 kN
Shear force at B VB = -5 kN
Bending moment at A MA = 0
Bending moment at C MC = RA *2 = 4*2 =8 kN-m
Bending moment at D MD = RA *4 – 3*2 =10 kN-m
Bending moment at B MB = 0

## Slide 23
Relations among load, shear and moment
dx
dx/2
wdx
M
M+dM
V
V+dV
dx
B
∑Fy = V + w dx - (V+dV) =0
dV = w dx
∑ MB = M + V dx + (w dx) dx/2 – (M + dM) =0
dM = V dx
V2 – V1 = ΔV = (Area)load
M2 – M1 = ΔM = (Area)shear

## Slide 24: Relation among Load Shear and Moment
Consider a simple beam shown of length L that carries a uniform load of w (N/m) throughout its length and is held in equilibrium by reactions R1 and R2.
R1 = R2 = wL/2

## Slide 25
Vx = R1 – wx = wL/2 – wx
Mx = R1 *x – w*x2/2
Mx = wLx/2 – w*x2/2
Differentiate M with respect to x
Thus, the rate of change of the bending moment with respect to x is equal to the shearing force, or the slope of the moment diagram at the given point is the shear at that point.

## Slide 26
Differentiating V with respect to x
Thus, the rate of change of the shearing force with respect to x is equal to the load or the slope of the shear diagram at a given point equals the load at that point.

## Slide 27: PROPERTIES OF SHEAR AND MOMENT DIAGRAMS
The following are some important properties of shear and moment diagrams:
The area of the shear diagram to the left or to the right of the section is equal to the moment at that section.
The slope of the moment diagram at a given point is the shear at that point.
The slope of the shear diagram at a given point equals the load at that point.
The maximum moment occurs at the point of zero shears.
When the shear diagram is increasing, the moment diagram is concave upward.
When the shear diagram is decreasing, the moment diagram is concave

## Slide 28: Draw SFD and BMD

## Slide 29
When x= 0; V = 1/6Lw0 = R1
X= L; V= -1/3Lw0 = -R2
Location of zero shear from left end V= 0 i.e. a = 0.577L
When x= 0; M =0
X= L; M=0
Moment at zero shear Mmax = 0.064L2w0

## Slide 31
w(x) | Concentrated load | UDL | Triangular
V(x) | Straight Line, No slope | Sloped Straight Line | Parabolic
M(x) | Sloped Straight Line | Parabolic | Cubic
Nature of Load, SF and BM

## Slide 32: Draw the SFD and BMD for the simple supported beam shown in figure below
1m
4m
3m
A
B
C
D
R1 =25 kN
R2 =15 kN
1m
4m
3m
A
B
C
D
R1
R2
10 kN/m
10 kN/m

## Slide 33
Shear force at A VA = RA = 25 kN
Shear force at C VC = 25 kN
Shear force at any section between C and D at a distance x from A
Vx = 25 – 10*(x – 1)
At D x = 5 and VD = 25 – 10*(5-1) = -15 kN
Shear force at B VB = -15 kN
Location of zero shear
0 = 25 – 10*(x-1)
x = 35/10 = 3.5 m from A
1m
4m
3m
A
B
C
D
R1
R2
10 kN/m

## Slide 34
Simply supported beam
Bending moment at A and B is 0
Bending moment at any section between C and D at a distance x from A
Mx = RA*x – 10* (x-1)*(x-1)/2
Mx = 25x – 5 (x-1)2
At C x = 1 MC = 25 kN-m
At D x = 5 MD = 25*5 – 5*(5-1)2 = 45 kN-m
B.M. at zero shear Mmax = 25*3.5 – 5*(3.5-1)2 = 56.25 kN-m
1m
4m
3m
A
B
C
D
R1
R2
10 kN/m

## Slide 37
Part AB
At x = 0 ft VAB = 670 – 60*0 = 670 lb
At x = 4 ft VAB = 670 – 60*4 = 430 lb
At x = 0 ft MAB = 0
At x = 4 ft VAB = 670*4 – 30*42 = 2200 lb-ft

## Slide 38
Part BC
At x = 4 ft VBC = -230 - 60*4 = -470 lb
At x = 12 ft VBC = -230 – 60*12 = -950 lb
At x = 4 ft MBC = 3600 - 230*4 – 30*42 = 2200 lb-ft
At x = 12 ft MBC = 3600 - 230*12 – 30*122 = -3480 lb-ft
Location of zero bending moment
MBC = 0 or x = 15.44 ft and 7.77 ft

## Slide 39
Part CD
MCD = 670x + 1710 (x-12) – 900(x-4) – 60x(x/2)
MCD = -16920 + 1480x – 30x2
VCD = 670 + 1710 – 900 – 60x
VCD = 1480 -60x
At x =12ft VCD = 1480 -60 * 12 = 760 lb
At x = 18 ft VCD = 1480 -60 * 18 = 400 lb
At x = 12ft MCD = -16920 + 1480*12 – 30*122 = -3480 lb-ft
At x = 18ft MCD = -16920 + 1480*18 – 30*182 = 0 lb-ft

## Slide 41
4ft
4k/ft
4ft
12k-ft
8ft
C
D
B
6K/ft
A
3ft
4ft
4k/ft
4ft
12k-ft
8ft
C
D
B
6/ft
A
3ft
RB
RC
RB= 19.42k, RC= 21.58K
∑MB= -½*3*6*(⅓*3)+4*8(4+4)+12 - RC*12=0

## Slide 42
4ft
4k/ft
4ft
12k-ft
8ft
C
D
B
6/ft
A
3ft
RB
RC
X=0.59ft
RB= 19.42k, RC= 21.58K
Shear at D VD = 0
Shear at C VC = -RC = -21.58K
E
Bending moment at D MD = -12 k-ft
Bending moment at C MC = -12 k-ft
Shear at E VE = -21.58 + 4*8 = 10.42K
Shear at B VB = -21.58 + 4*8 – 19.42 = -9 K
Shear at A = 0
Location of zero shear between C and E
-21.58 + 4*x = 0; x = 5.4 ft from C
Bending moment at B MB = -12 + (21.58*12) – 4*8* (4+8/2) = - 9 k-ft
Bending moment at E ME = -12 + (21.58*8) – 4*8*8/2 = 32.64 k-ft
Maximum moment Mmax = -12 + 21.58*5.4 – 4*5.4*5.4/2 = 46.2 k-ft

## Slide 43
4ft
4k/ft
4ft
12k-ft
8ft
C
D
B
6K/ft
A
3ft
9K
10.42K
21.58K
0.0 K
Dangerous section
2.6ft
-ve
+ve
-ve
SFD
12k-ft
32.64 k-ft
9k-ft
46.23-ft
3.14ft
Point of inflection
Point of inflection
0.59ft
+ve
-ve
-ve
BMD

## Slide 45
RA
RH
4000 lb
4ft
4ft
∑MA = 0; 4000*4 - RH*8 = 0
RC =4800 lb
RD =1200 lb
RH = 2000 lb
∑MD = 0; RC*10 - 4000*5 -2000*14 = 0
RH = 2000
RD
4000 lb
5ft
5ft
4ft
RC

## Slide 46
RA
RH
4000 lb
4ft
4ft
2000
1200
400 lb/ft
4ft
4800
7ft
1200
2000
2800
8000
1800
16000
2000
2000

## Slide 48
Free body diagram
∑MA = 0 ; Dy = 11.84 k
Ay = 4.16 k
Ax = -9.6 k

## Slide 50
∑MB = 0 ; MB = 76.8 k-ft
By = -4.16 k
Bx = 0k
Vy = 9.6 – 0.6 x
My = 9.6*x – (0.6 x*x/2)

## Slide 51
Cx = 0k

## Slide 52
Vx = 4.16 – 0.8 x
Mx = 4.16*x + 76.8 – (0.8 x*x/2)

## Slide 53
Free body diagram
SFD
BMD

## Slide 54
24kN/m
B
4m
3m
2m
2m
60kN
D
A
C

## Slide 55
A
24kN/m
B
C
4m
3m
2m
2m
60kN
Ay
Cy
Ax
∑MA = 0; 60*2 + 24*4*(4+4/2) – Cy *8 = 0
∑Fy = 0; Ay = 69 kN
Cy = 87 kN
∑Fx = 0; Ax = 0 kN

## Slide 56
A
24kN/m
B
C
4m
3m
2m
2m
60kN
Ay
Cy
θ
cos θ = 4/5
sin θ = 3/5
A1
A2
F1
F2
A2 = -Ay sin θ = - 69* 3/5 = -41.4 kN
A1 = Ay cos θ = 69* 4/5 = 55.2 kN
F2 = -60 sin θ = - 60* 3/5 = - 36 kN
F1 = 60cos θ = 60* 4/5 = 48 kN
D

## Slide 57
55.2
A2
48kN
55.2
7.2
MA = 0
MD = 55.2* 2.5 = 138 kN-m
MB = 55.2* 5 – 48*2.5 = 156 kN-m
156
138
V
M
D
∑MB = 0; 55.2*2.5- 48*2.5 –M = 0
M = 156 kN-m

## Slide 58
24kN/m
B
C
87 kN
M
FB = 7.2/cosθ = 9 kN
FB = 87 – 24*4 = 9 kN
Vx = 9 – 24*x
Mx = 156+ 9*x – 24*x*x/2

## Slide 59
24kN/m
B
C
87 kN
M
Chart: 
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
V | 9 | -3 | -15 | -27 | -39 | -51 | -63 | -75 | -87
Chart: 
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
M | 156 | 157.5 | 153 | 142.5 | 126 | 103.5 | 75 | 40.5 | 0

## Slide 60
SFD
BMD

## Slide 61
VE =63.24k
RF =27.36k
7k
5k/ft
4
3
A
B
C
D
E
F
HE=4.2k
12ft
5ft
4ft
14ft
14ft
63.24k
27.36k
-ve
+ve
+ve
-ve
21.76k
5.6k
38.24k
25k
7.65ft
Dangerous section
62.5k-ft
121.3k-ft
24.97k-ft
22.4k-ft
Point of inflection
Point of inflection
-ve
-ve
+ve
SFD
BMD
7k
A
4ft
5k/ft
B
C
D
12ft
5ft
5.6k
63.24k
4.2k
B
E
0.0 k
BMD
27.36k
C
F
SFD
0.0 k