## Slide 1
Turbulent Flow
In a pipe, turbulent flow occurs when
In a turbulent flow, fluid motion is irregular and chaotic and there is complete mixing of fluid due to collision of fluid masses with one another.
The fluid masses are interchanged between adjacent layers.
As the fluid masses in adjacent layers have different velocities, interchange of fluid masses between the adjacent layers is accompanied by a transfer of momentum.
The shear in turbulent flow is mainly due to momentum transfer.

## Slide 2: Transfer of Momentum in Turbulent flow

## Slide 3
Velocity distribution curve for Laminar and Turbulent flow
The velocity distribution in turbulent flow is more uniform than in laminar flow.
In turbulent flow, the velocity gradients near the boundary wall shall be quite large resulting in more shear.
In turbulent flow, the flatness of velocity distribution curve in the core region away from the wall is because of mixing of fluid layers and exchange of momentum between them.
The velocity distribution which is paraboloid in laminar flow tends to follow logarithmic variation in turbulent flow.
Random orientation of fluid particles in a turbulent flow gives rise to additional stresses, called Reynolds stresses.

## Slide 4: Velocity Distribution Curve

## Slide 5
Laminar-Turbulent
A laminar flow changes to turbulent flow when-
Velocity is increased.
Diameter of pipe is increased.
Viscosity of fluid is decreased
Frictional resistance for turbulent flow is:
Proportional to ; where n varies from 1.5 to 2.0.
Proportional to the density of fluid.
Proportional to the area of surface in contact.
Independent of pressure.
Dependent on the nature of surface in contact.

## Slide 6
Loss of Head due to Friction in Pipe flow (Darcy Equation)
Notation | Parameter
 | Intensity of Pressure at section 11
 | Velocity of flow at section 11
, | Intensity of pressure and Velocity of flow at section 22 respectively.
L | Length of the pipe between section 11 and 22
d | Diameter of the pipe
 | Frictional resistance per unit wetted area per unit velocity
 | Loss of head due to friction
Notation | Parameter
L | 
d | Diameter of the pipe
 | Frictional resistance per unit wetted area per unit velocity
 | Loss of head due to friction

## Slide 7
Forces acting on the fluid between section 11 and 22;
Pressure force at section 1 =
Pressure force at section 2 =
Frictional resistance
Resolving all the forces in horizontal direction:
A (
( ………………………. (1)
Loss of Head due to Friction in Pipe flow (Darcy Equation)

## Slide 8
Let, = loss of head due to friction.
= = 0 ;
………………….. (2)
Applying Bernoulli's equation at section 11 and 22;
Applying Bernoulli's equation at section 1−1 and 2−2;

## Slide 9: Frictional Resistance,
Frictional resistance
= frictional resistance per unit wetted area per unit velocity wetted area
=
= P (Perimeter , P = )
From equation 1 and 2, we get,

## Slide 10: Darcy Weisbach Equation
Hydraulic mean depth,
R =
Putting
Loss of head due to friction in pipes flow,