## Slide 1: Factors influencing Hydraulic Phenomena
1. Inertia force ():
It always exists in the fluid flow problem.
It is equal to the product of mass and acceleration of the flowing fluid and acts in the direction opposite to the direction of acceleration.
Inertia force, = mass acceleration
2. Viscous force ():
It is present in fluid flow problems where viscosity is to play an important role.
It is equal to the product of shear stress (τ) due to viscosity and surface area of flow.
Viscous force, = shear stress surface area

## Slide 2: Factors influencing Hydraulic Phenomena
3. Gravity force ():
It is present in case of open surface flow.
It is equal to the product of mass and acceleration due to gravity.
Gravity force, = mass acceleration due to gravity
4. Pressure force ():
This type of force is present in case of pipe flow.
It is equal to the product of pressure intensity and cross-sectional area of the flowing fluid.
Pressure force, = pressure intensity cross-sectional area

## Slide 3: Factors influencing Hydraulic Phenomena
5. Surface tension force (
It is equal to the product of surface tension and length of surface of the flowing fluid.
= surface tension length of surface of flowing fluid
6. Elastic Force ():
It is equal to the product of elastic stress and area of the flowing fluid.
= elastic stress area of flowing fluid

## Slide 5: Dimensionless numbers and their significance
Reynolds number
Froude’s number
Euler’s number
Weber’s number
Mach’s number

## Slide 6: Reynolds Number,
Reynolds from his experiment, found that the nature of flow in a closed conduit depends upon the following factors:
Diameter of the pipe (D)
Density of the liquid (ρ)
Viscosity of the liquid (μ)
Velocity of flow (V)
By combining the above variables, Reynolds determined a non-dimensional quantity equal to which is known as Reynolds number.

## Slide 7: Reynolds Number,
It is defined as the ratio of inertia force to the viscous force.
Inertia force
= density volume
= density Velocity
= density Area Velocity Velocity
= ρA

## Slide 8: Reynolds Number,
Viscous force
= µ
= µ
Reynolds Number , = =

## Slide 9: Froude Number
It is defined as the square root of the ratio of inertia force and the gravity force.
Mathematically, =
Here, inertia force, = ρA
Gravity force,
= Mass Acceleration due to gravity
= density volume g
= ρ AL g
=

## Slide 10: Euler’s Number
It is defined as the square root of the ratio of the inertia force to the pressure force.
Mathematically, =
Here, inertia force, = ρA
Pressure force,
= intensity of pressure area
= P A
=

## Slide 11: Weber Number
It is defined as the square root of the ratio of the inertia force to the surface tension force.
Mathematically, =
Here, inertia force, = ρA
Surface tension force,
= surface tension length
= σ L
=

## Slide 12: Mach Number
It is defined as the square root of the ratio of the inertia force to the elastic force.
Mathematically, M =
Here, inertia force, = ρA
Elastic force,
= elastic stress area
= K A = K
M = ; C = Velocity of sound in the fluid

## Slide 13: Summary