## Slide 1: Flow through Orifice and Mouthpieces
Classification of Orifice
Flow through an orifice
Hydraulic Coefficients ( )
Experimental Determination of Coefficients
Discharge through a large rectangular orifice
Classification of Mouthpiece
Discharge through an external mouthpiece

## Slide 2: Orifice
An orifice is an opening in the wall or base of a vessel through which fluid flows.
The top edge of orifice is always below the free surface.
Orifices are used to measure the discharge of fluid flow.

## Slide 3: Classification of Orifice
Parameter | Type of Orifice
According to Size | Small orifice
 | Large orifice
According to Shape | Circular Orifice
 | Rectangular Orifice
 | Square Orifice
 | Triangular Orifice
Shape of Upstream edge | Sharp Edged Orifice
 | Bell Mouthed Orifice
According to Discharge Condition | Free Discharge Orifice
 | Submerged Orifice
 | Fully Submerged Orifice
 | Partially Submerged Orifice

## Slide 4: Torricelli’s Theorem (flow through an orifice)
Consider two points 1 and 2 as shown in figure.
Point 1 is inside the tank and point 2 at the vena contracta.
Let the flow is steady and at a constant head H. Applying Bernoulli’s equation at point 1 and point 2 gives:

## Slide 5: Torricelli’s Theorem

## Slide 6: Hydraulic Coefficients ( )
Co-efficient of Contraction:
The ratio of area of jet at vena contracta to the area of the orifice is known as co-efficient of contraction. It is denoted by .
= =

## Slide 7: Hydraulic Coefficients ( )
Co-efficient of resistance:
The ratio of loss of head in the orifice to the head of water available at the exit of the orifice is known as co-efficient of resistance. It is denoted by .
=

## Slide 8: Relationship:

## Slide 9: Standard Value for Hydraulic Coefficients
Hydraulic Coefficients | Range of Values
Co-efficient of Velocity | 0.95-0.99
Co-efficient of Contraction | 0.61-0.69
Co-efficient of Discharge | 0.61-0.65

## Slide 10: Practice Problem#9 (Rajput 495 page)
An orifice 60 mm in diameter is discharging water under a head of 9 meters. If = 0.60 and = 0.90 find:
Actual Discharge
Actual Velocity of Jet at Vena- Contracta
Answer:
0.02254 /s
11.26 m/s

## Slide 11: Experimental Determination of Hydraulic Coefficients
1. Determination of Co-efficient of Velocity by Co-ordinate method
=
2. Determination of Co-efficient of Discharge
=
Value of Actual Discharge is determined with the help of a rectangular tank.

## Slide 12: Practice Problem#10 (Bansal)
A tank has two identical orifices on one of its vertical sides. The upper orifice is 3 meter below the water surface and lower one is 5 meter below the water surface. If the value of for each orifice is 0.96, find the point of intersection of two jets.

## Slide 13: Solution

## Slide 15: Practice Problem#11 (Rajput, Page= 457)
A 3 m tank standing on the ground is kept full of water. There is a small orifice in its vertical side with its center at depth h meters below the free surface of liquid in the tank. Find the value of h so that the liquid strikes the ground at the maximum distance from the tank. Assuming Cv= 0.97, calculate the maximum value of horizontal distance.

## Slide 16: Practice Problem#11 (Rajput, Page= 457)