## Slide 1
Group-2
Rajshahi University of Engineering & Technology
DEPARTMENT OF CIVIL ENGINEERING

## Slide 2
Course code: CE 3218
Course Title : Reinforced Concrete Sessional-II
Submitted By
1700074,1700075,1700076,1700077,
1700078,1700079,1700080,1700081,
1700082,1700083,1700084,1700085,
1700086
Submitted To
Dr. Abu Sufian Md. Zia Hasan
Professor, Civil Engineering
Rajshahi University of Engineering & Technology
Group: 02

## Slide 3
Footing Design of a Two Storied Residential Building
PRESENTATION ON

## Slide 4
What is footing
Footing is a part of foundation which is constructed with reinforced concrete or brickwork masonry and acts as a base to the floor columns and floor walls.
The main function of footing is to transfer the vertical loads directly to the soil.

## Slide 5: Some pictures of footing in RUET

## Slide 8
The objectives of footing
To distribute the load of structure over the large bearing area.
To increase the stability of the structure as a whole.
To prevent unequal settlement.
To prevent the lateral movement of the supporting material.

## Slide 9: Types of footing
Wall footing
Single column footing
Combined footing
Strap footing
Mat or raft footing

## Slide 10: Wall footing
A wall footing is a continuous strip of reinforced concrete wider than the wall that distributes pressure.

## Slide 11: Single column footing
They are usually square, sometimes rectangular and represent the simplest and most economical type.
When footing is provided to support an individual column, it is called isolated or single column footing.

## Slide 12: Combined footing
Combined footings are constructed for two or more columns when they are close to each other and their foundations overlap.

## Slide 13: Strap footing
It consists of two single column footing connected with a structural strap. The strap connects the footing such that they behave as one unit.
A strap footing is more economical than combined footing.

## Slide 14: Mat or raft footing
It is a large soil reinforced concrete slab that extends under the entire building and consequently distributes the load of the structure over the maximum available area. Such foundation minimizes differential settlement.
A mat is required when the allowable soil pressure is low or where the columns and walls are so close that individual footings overlap or nearly touch each other.

## Slide 16: Types of failure of a footing
There are three types of failure of a footing-
General shear failure
Local shear failure
Punching shear failure

## Slide 17: Footing design of a two storied residential building

## Slide 18: Ground floor plan

## Slide 19: First floor plan

## Slide 20: Column footing layout

## Slide 21: The design steps
Calculation of ultimate bearing capacity
Punching shear check
Beam shear check
Moment Calculation
Reinforcement Calculation
Working Diagram

## Slide 22
STEEL SPECIFICATION : = 60 ksi ; = 3 ksi
Footing Types : F1 , F2 , F3 (Total 16 Footings in the Plan )
Footing Sizes : (b x b x Thickness of Footing )
F1 : 4‘ x 4’ x 7’’ [b=4 ft] 4 no. F1 footings
F2 : 5’ x 5’ x 8” [b=5 ft] 8 no. F2 footings
F3 : 6’ x 6’ x 9” [b=6 ft] 4 no. F3 footings
Specifications For Footing
Allowable Bearing Capacity of Soil : qall = 2 k/ft2
Depth of Footing : Df = 5 ft

## Slide 23
Specifications For Footing
Fill of Soil on the top of footings : (Dfill )
F1 : (5 - ) = 4.42 ft
F2 : (5 - ) = 4.33 ft
F3: (5 - ) = 4.25 ft
Column Size :
C1 : x
C2 : x
C3 : x
For all columns ,
a = 12 inch = 1 ft (Minimum according to BNBC )
Load Data :
F1 : Dead Load = 14 kips , Live Load = 8 kips
F2 : Dead Load= 20 kips , Live Load = 12 kips
F3 : Dead Load = 30 kips , Live Load = 18 kips

## Slide 24
12 in.
7 in.
b = 4 ft
= 2 k/
F1 Footing Design

## Slide 25
F1 Footing Design
STEEL SPECIFICATION : = 60 ksi; = 3 ksi
Load : DL = 14 kips ; LL = 8 kips
Footing Sizes :
Ultimate bearing pressure ,
qu = = = 1.85 k/ft2
Punching Shear Check:
The length of the critical perimeter, bo = 4(12+d)
4 ft
12’’
d1
1.5ft
d
b
a
c
d
e
f
h
g

## Slide 26
F1 Footing Design
The shear acting on this perimeter ,
Vu1= qu [b2 -2]
= 1.85 x[42 -2]
= 29.6 - (122+24d+d2)
= 29.6 – 1.85 – 0.31d – 0.0128d2
= 27.5 – 0.31d – 0.0128d2
The design shear , øVc = =
= 7.89 d + 0.657d2
From which ,
27.75 – 0.31d – 0.0128d2 = 7.89 d + 0.657d2
Or, 0.6698d2 + 8.2d – 27.75 = 0
d= 2.76 inch 3 inch

## Slide 27
F1 Footing Design
Vu1 = 1.85 x[42 -2]= 26.71 kips
So, øVc = = 29.58 kips
Since , øVc > Vu1
the depth d= 3 inch is adequate for punching shear
Therefore , Design is Ok
Beam Shear Check :
d1 = (48- 18-12-3)= 15 inch
Vu2 = qu bd1
= 1.85 x 4 x
= 9.25 kips
The design shear ,
øVc = = = 11.831 kips
Since , øVc > Vu2
Therefore , Design is Ok

## Slide 28
F1 Footing Design
Moment Calculation :
= = = 8.325 k-ft
Reinforcement Calculation :
a= = = 0.4902 As
= 0.2451As
As = = = 0.651 in 2
As (min)= = = 0.3944 in2
But not less than, As (min)= = = 0.48 in2
And , As (min)= 0.0025bt = 0.0025 X (4X12)X7 = 0.84 in2
Hence , the required area is 0.84 in2
Provide , 7 #6 bars @ = 6.28

## Slide 29
REINFORCEMENT DETAILS of F1 FOOTING

## Slide 30
F2 Footing Design
12 in.
8 in.
b = 5 ft
= 2 k/

## Slide 31
F2 Footing Design
STEEL SPECIFICATION : = 60 ksi ; = 3 ksi
Load : DL = 20 kips ; LL = 12 kips
Footing Sizes :
Ultimate bearing pressure ,
qu = = = 1.728 k/ft2
Punching Shear Check:
The length of the critical perimeter, bo = 4(12+d)
5 ft
12’’
d1
2 ft
d
b
a
c
d
e
f
h
g

## Slide 32
F2 Footing Design
The shear acting on this perimeter ,
Vu1= qu [b2 -2]
= 1.728 x[52 -2]
= 43.2 - (122+24d+d2)
= 43.2 – 1.728 – 0.288d – 0.012d2
= 41.472 – 0.288d – 0.012d2
The design shear , øVc = =
= 7.89 d + 0.657d2
From which ,
41.472 – 0.288d – 0.012d2 = 7.89 d + 0.657d2
Or, 0.669d2 + 8.178d – 41.472 = 0
d= 3.86 inch 4 inch

## Slide 33
F2 Footing Design
Vu1 = 1.728 x[52 -2]= 40.128 kips
So, øVc = = 42.065 kips
Since , øVc > Vu1
the depth d= 4 inch is adequate for punching shear
Therefore , Design is Ok
Beam Shear Check :
d1 = (60 -24-12 - 4)= 20 inch
Vu2 = qu bd1
= 1.728 x 5 x
= 14.4 kips
The design shear ,
øVc = = = 19.72 kips
Since , øVc > Vu2
Therefore , Design is Ok

## Slide 34
F2 Footing Design
Moment Calculation :
= = = 17.28 k-ft
Reinforcement Calculation :
a= = = 0.392 As
= 0.196As
As = = = 1.01 in 2
As (min)= = = 0.66 in2
But not less than, As (min)= = = 0.80 in2
And , As (min)= 0.0025bt = 0.0025 X (5X12)X8 = 1.20 in2
Hence , the required area is 1.20 in2
Provide , 14 # 6 bars @ = 4.40

## Slide 35
REINFORCEMENT DETAILS of F2 FOOTING

## Slide 36
F3 Footing Design
12 in.
9 in.
b = 6 ft
= 2 k/

## Slide 37
F3 Footing Design
STEEL SPECIFICATION : = 60 ksi ; = 3 ksi
Load : DL = 30 kips ; LL = 18 kips
Footing Sizes :
Ultimate bearing pressure ,
qu = = = 1.80 k/ft2
Punching Shear Check:
The length of the critical perimeter, bo = 4(12+d)
6 ft
12’’
d1
2.5 ft
d
b
a
c
d
e
h
f
g

## Slide 38
F3 Footing Design
The shear acting on this perimeter ,
Vu1= qu [b2 -2]
= 1.8 x[62 -2]
= 64.8 - (122+24d+d2)
=64.8 – 1.8 – 0.3d – 0.0125d2
= 63– 0.3d – 0.0125d2
The design shear , øVc = =
= 7.89 d + 0.657d2
From which ,
63– 0.3d – 0.0125d2 = 7.89 d + 0.657d2
Or, 0.6695d2 + 8.19d – 63 = 0
d= 5.35 inch 6 inch

## Slide 39
F3 Footing Design
Vu1 = 1.8 x[62 -2]= 60.75 kips
So, øVc = = 70.98 kips
Since , øVc > Vu1
the depth d= 6 inch is adequate for punching shear
Therefore , Design is Ok
Beam Shear Check :
d1 = (72 -30 -12 - 6)= 24 inch
Vu2 = qu bd1
= 1.8 x 6 x
= 21.6 kips
The design shear ,
øVc = = = 35.49 kips
Since , øVc > Vu2
Therefore , Design is Ok

## Slide 40
F3 Footing Design
Moment Calculation :
= = = 33.75 k-ft
Reinforcement Calculation :
a= = = 0.327 As
= 0.163As
As = = = 1.30 in 2
As (min)= = = 1.18 in2
But not less than, As (min)= = = 1.44 in2
And , As (min)= 0.0025bt = 0.0025 X (6X12)X9 = 1.62 in2
Hence , the required area is 1.62 in2
Provide , 22 # 6 bars @ = 3.26

## Slide 41
REINFORCEMENT DETAILS of F3 FOOTING

## Slide 42: Conclusions
Footing is one of the most necessary element of Civil Engineering since all the structures are to be built on sub-structure.
The structure may be strong but for the durability and stability of the structure its footing needs to be strong enough for which one should have thorough knowledge of foundation engineering.
All the load of structure is lastly transmitted to the column footing so it should have enough strength to take that load without any settlement of the footing.

## Slide 43: Thank you