## Slide 1: Write a C program to calculate shear force and bending moment at any point for the following beam.
w1 unit per feet
w2 unit per feet
A
C
B
Beam Portion | Loading Condition | Length
AC | w1 unit per feet | 10 feet
CB | w2 unit per feet | 10 feet

## Slide 2: Program
Step 1: Find the reaction of the beam
Let us consider,
Reaction at A = r1
Reaction at B = r2
So, after calculating,
r2 = (2.5*w1)+ (7.5*w2)
r1 = (7.5*w1) + (2.5*w2)

## Slide 3
Condition | Shear force | Bending Moment
x==0 | 0 | 0
x>0 && x<=10 | r1-(w1*x) | (r1*x)-(w1*x*x*0.5)
x>10&&x<20 | r1-(w1*10)-(w2*(x-10)) | (r1*x)-(10*w1*(x-5))-(w2*(x-10)*(x-10)*0.5)
x==20 | 0 | 0

## Slide 4: Recommended problems
Practice each of these problems.
http://www.mediafire.com/file/31esyx7mqthm70t/Beam_Analysis.pdf/file
The more you practice, the more you can learn.