## Slide 1
EFFECTS OF IMPACT LOAD AND CONSTRUCTON METHODS OF BRIDGE
GROUP: A-04
ROLL: 130031-13040

## Slide 2
our presentation is in two segments
1st one : effects of various types of impact load on bridge
2nd one : various types of construction methods all over the world

## Slide 3
Impact load:
The dynamic effect on a structure, either moving or at rest, of a forcible momentary contact of another moving body in a short time.
types of Impact load on bridge:
earthquake
wind effect
live load
Effects of various types of impact load on bridge

## Slide 4: How do earthquakes affect on bridges

## Slide 5
In the last few years in the Indian subcontinent, we have been experiencing a significant increase in the frequency and magnitude of earthquakes.
There are many who say that this is the result of the exploration for underground gas reserves, which has become widespread in this area.
No matter the root cause, the subject of how earthquakes affect bridges is now on the minds of many.

## Slide 6
When evaluating the affects of earthquakes the most important factors to take into account are the magnitude of the earthquake, the distance from the epicenter of the earthquake and the geologic conditions at the site of the earthquake itself.
When it comes to how earthquakes can affect bridges, the main concern is the damage that can be caused by the ground motion that the earthquake creates.

## Slide 7
When soft soil lies on top of hard bedrock the ground motion is amplified, this is known as ground-motion amplification.
This type of amplification can result in much greater damage, even from bridges that are quit a distance from the epicenter of the earthquake itself.
In fact, soft sandy soils can actually be liquefied by strong ground motion in a process call liquefaction.

## Slide 8
When liquefaction occurs, the foundation of structures, like bridges, can be completely compromised.
Whether Earthquakes Affect Bridges Depends Greatly On the Magnitude.
The general rule of thumb is that earthquakes below a magnitude of 4.0 do not cause infrastructure damage.
Highway engineers have devised standards in an attempt to earthquake-proof bridges that have been built since the early 1990's.

## Slide 9
TONGJI BRIDGE, CHINA
Overview Pounding Damage at Railing Joints

## Slide 10
XIAOYUDONG BRIDGE, CHINA
Damage in Easternmost Details of Shear Failures
Span

## Slide 11
Flexural Crack on Pile Shaft Transverse Crack on Top of the Bridge Deck
XIAOYUDONG BRIDGE, CHINA

## Slide 12
Wind Effect On BRIDGE
Wind produces 3 types of effects on structure. They are :
Static
Dynamic
Aerodynamic
When the structure deflects in response to wind load then the dynamic and aerodynamic effects should be analysed in addition to static effect.actually wind creat aerodymanic effect on bridge as impact load.

## Slide 13: Bridge aerodynamics and wind induced vibrations:
1.Galloping: Galloping is transverse oscillation of some structures due to the development of aerodynamic forces. Non circular cross section are more susceptible to this type of oscillation.
Tacoma Narrows Bridge, Washington
Figure : Galloping effect

## Slide 14
2.Flutter: Flutter is unstable oscillatory motion of a structure due to coupling between aerodynamic force and elastic deformation of the structure.
In case of classical flutter, energy is fed by wind counteracting the damping of the bridge. With the increase in the speed of incoming wind, the dumping of the structure increases.
Tacoma Narrows Bridge, Washington
Figure: Fluttering effect
Notes: Figure: Fluttering effect

## Slide 15
Effect of live load on bridge as impact load
impact load:
The dynamic effect caused due to vertical oscillation and periodical shifting of live load from one wheel to another is known as impact load.
According to AASTHO impact factor is expressed as a function of bridge span which is given below-
Impact Factor, I = ≤ 0.30
Here, L is the length in feet of the section of span that must be loaded to produce the maximum stress in a particular member.

## Slide 16: Major characteristics of impact factor:
1. Impact factor increases as vehicle speed increases in most cases. 2. impact factor decreases as bridge span increases. 3.impact factor decreases as vehicle travel in more than one lane. 4.impact factor for exterior girder is much more larger than for interior girder due to the excided torsion mode shapes contribute to the dynamic response of exterior girder. 5.Under very good condition of the road surface roughness impact factor is well below that in design specifications.

## Slide 17: Impact percentage curve: Impact factors are specified by different authorities for different types of bridges. The following curve shows the relationship between impact factor and span of the bridge…

## Slide 18
Limit state | Impact factor
Deck joint | 75%
Fracture limit state | 15%
All other limit state | 33%
Impact factor for various limit state according to AASTHO

## Slide 19: Effect of impact load
Impact factor is considered for vibration induced by truck on bridge
Vehicular live loads are multiplied with an impact factor to accommodate this dynamic effect in the design of bridge. The dynamic loads for moving vehicle are considered impact in bridge engineering because of relatively short duration.

## Slide 20
various types of construction methods all over the world
Second segment

## Slide 21
Bridge Construction Methods
Pre-cast
1. I Beams & Super Tee’s
2. Segmental
3. Full Span
ii. Cast in-situ
iii. Others

## Slide 22
Precast I Beams & Super Tee’s
Cebu South Coastal Road -Philippines

## Slide 23
Precast Segmental Techniques
1. Description
• Complete deck cast, delivered & erected in unique cells
• Segments are prestressed together using external and
or internal tendons. Joints can be “dry” or “wet”.
• Typically in Span by Span or Balanced Cantilever mode
2. Advantages
•Structurally efficient and aesthetic
•Complete with deck when erected I.e. rapid & safe
•Cast during substructure works – overlap of activities

## Slide 24
PRECAST SEGMENTAL ERECTION TECHNIQUES
Erection on Falsework
Erection by Gantry
Erection by Crane
Erection by Lifting Frame
Full Span Erection Techniques

## Slide 25
1. ERECTION ON FALSEWORK

## Slide 26
2. ERECTION BY GANTRY
A. Span By Span – “Simply Supported

## Slide 27
B. Balanced Cantilever

## Slide 28
3. ERECTION BY CRANE

## Slide 29
4. ERECTION BY LIFTING FRAME

## Slide 30
5. FULL SPAN PRECAST ERECTION TECHNIQUES

## Slide 31
IN-SITU CONCRETE BRIDGES CONSTRUCTION TECHNIQUES.
1.Cast in-situ Post Tensioned
2.Balanced Cantilever
3.Incrementally Launched

## Slide 32
Cast in-situ Post tensioned

## Slide 33
2. BALANCED CANTILEVER
Cast In-situ

## Slide 34
3. INCREMENTAL LAUNCHED Cast In-situ

## Slide 35
Others
•glass bridge
•Pier Head Rotation
•Arch Lowering
•Main Span Lifting
•Skybridge

## Slide 36
Glass bridge

## Slide 37
Location: Zhangjiajie Grand Canyon in Hunan’s picturesque, Zhangjiajie National Park,chaina
Construction duration: 2009-2016
Architect: Haim Dotan, Israel
Length: 1411ft
Height: 984ft
Carring capacity:800 people at a time
Some information about this glass bridge:

## Slide 38
Thank you